## Slide 1: New opportunities for in situ sampling of water and carbon-dioxide isotopologues within the soil and atmosphere at LEO

## Slide 2
Why measure soil water and CO2 isotopes in LEO basalt (and atmosphere)?
Isotopic analyzer
Sampling set up for soil air CO2 and vapor
Inference of liquid water isotopes
Atmospheric sampling
(Potential scheme for soil gas sampling)

## Slide 3: Sampling H2O isotopologues at LEO - What can we learn?
Pathways of water through the hillslope – time evolution, interaction with weathering
Subsurface mixing and transport at scale of soil profiles to hillslope
Transit times and age distribution of water
Evapotranspiration

## Slide 4: Sampling CO2 isotopologues at LEO - What can we learn?
Contribution of chemical and biological process to carbon dynamics
Limiting effect of CO2 diffusion from atmosphere for carbon uptake within slope
Equilibrium of gas-phase CO2 with the solution phase
Carbonate precipitation within the slope
Plant uptake of CO2 from the atmosphere

## Slide 5: Aerodyne real-time dual continuous wave quantum cascade laser
Continous analyis of gas stream
Fast time response
Two characterized IR tunable lasers
  CO2, 13CO2, CO18O with one laser
    δ18O-CO2 with σ(1 Hz) < 0.1 ‰
    δ13C-CO2 with σ(1 Hz) < 0.1 ‰
  H2O, HDO, H218O with second laser
    δ18O-H2O with σ(1 Hz) < 0.1 ‰
    δD-H2O with σ(1 Hz) < 0.3 ‰

## Slide 6: Automated sampling of soil air with direct isotopic analysis
151 soil gas probes/slope
  Microporous PTFE tubing (30cm exchange loop)
  sealed at both ends to gas transport lines
Closed loop sampling  full equilibration

## Slide 7: Automated sampling of soil air with direct isotopic analysis
151 soil gas probes/slope
  Microporous PTFE tubing (30cm exchange loop)
  sealed at both ends to gas transport lines
Closed loop sampling  full equilibration
Dilution  condensation prevention

## Slide 8: Automated sampling of soil air with direct isotopic analysis
151 soil gas probes/slope
  Microporous PTFE tubing (30cm exchange loop)
  sealed at both ends to gas transport lines
Closed loop sampling  full equilibration
Dilution  condensation prevention
Shed with AC  temperature stability

## Slide 9: Automated sampling of soil air with direct isotopic analysis
151 soil gas probes/slope
  Microporous PTFE tubing (30cm exchange loop)
  sealed at both ends to gas transport lines
Closed loop sampling  full equilibration
Dilution  condensation prevention
Shed with AC  temperature stability
Multi-valve system  automated sampling

## Slide 10: Automated sampling of soil air with direct isotopic analysis
Ca. 4 min/sample
No manual sample collection or lab analysis
Small sample volumes
Simultaneous isotope data for CO2 and water vapor in soil air + Inference of liquid water isotopic composition

## Slide 11: Inference of liquid soil water isotopic composition from vapor
Vapor typically in isotopic equilibrium with liquid water
 Liquid water composition can be infered if temperature-dependent equilibrium fractionation factor is known
Horita & Wesolowski, Geochim. Cosmochim. Acta 58, 3425-3437 (1994).
Soderberg et al., Vadose Zone J. 11 (2012).
Free water
Soil

## Slide 12: Inference of liquid soil water isotopic composition from vapor
Potential effects on αE in soils: water activity (salts, matric potential), structural change in confined space, hydration sphere isotope effect  minor at MP > -10 MPa and low clay content
Potential sampling induced mixing  can be avoided
Soderberg et al., Vadose Zone J. 11 (2012).
Volkmann & Weiler, HESS 18, 1819-1833 (2014).

## Slide 13: Inference of liquid soil water isotopic composition from vapor

## Slide 14: Atmospheric sampling
Exisiting gas sampling set up for 24 locations/slope
Flow cell 1/e time response (s): 0.1 sec (300 lpm)
Evapotranspiration, CO2 fluxes and plant uptake

## Slide 15: Potential soil gas sampling locations

## Slide 16: Location-Time resolution trade-off for soil gas sampling
Which processes to investigate?
What is their temporal scale?
All locations
1 slope
All locations
3 slopes

## Slide 17: Potential scheme for soil gas sampling
50-150 locations per slope b/w events  10-30 h time step
10-15 locations on 1 slope during rainfall  1 h time step